| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING TOKYO, JAPAN, 1 - 5 JULY 2013 |  | IPET-DRMM-I / Doc. x.x (x) (xx. x. 2013) ------------------------- ITEM x.x ENGLISH ONLY |
| --- | --- | --- |

JCOMM Recommendations on the migration to Table Driven Code Forms.

Submitted by the JCOMM Representative, David Berry (United Kingdom)

_______________________________________________________________________

Summary and Purpose of Document

This document summarizes JCOMM proposals to the CBS with regard to the migration from Traditional Alphanumeric Codes and Table Driven Code forms.

_______________________________________________________________________

ACTION PROPOSED

The Team will review the information contained in this report, and comment and make decisions or recommendations as appropriate. See part A for the details of recommended actions. Proposed BUFR templates are defined in Part B, proposed changes to the WMO Manual on Codes in Part C and changes to the BUFR / CREX regulations B/C 10 in part D.

APPENDICES: 2

PART A - DISCUSSION

ENCODE Proposal

A separate document describing the JCOMM Proposal for the encryption of ship's callsigns within BUFR reports has been submitted (IPET-DRMM-I / Doc x.x (x)). The team are invited to review, comment and make recommendations on the ENCODE proposal. The team are also invited to advise whether the proposed governance of the encryption keys should be made to the WMO EC via the CBS or via JCOMM.

The proposed changes to the WMO Manual on Codes to accommodate the ENCODE proposal are described in Doc x.x but are also included in Part C of this report for completeness.

Migration to TDCFs

The following Traditional Alpha-Numeric Codes (TAC) are used operationally for the distribution of time-critical maritime observations through the Global Telecommunication System (GTS):

- FM 13–XIV SHIP - Report of surface observation from a sea station

- FM 18-XII BUOY – Report of a buoy observation

- FM 36–XI Ext. TEMP SHIP - Upper-level pressure, temperature, humidity and wind report from a sea station

- FM 62–VIII Ext. TRACKOB - Report of marine surface observation along a ship’s track

- FM 63–XI Ext. BATHY - Report of bathythermal observation

- FM 64–XI Ext. TESAC - Temperature, salinity and current report from a sea station

- FM 65-XI Ext. WAVEOB – Report of spectral wave information from a sea station or from a remote platform (aircraft or satellite)

These codes are managed by the WMO Commission for Basic Systems (CBS) and described in the WMO Publication No 306, WMO Manual on Codes. However, in the view to promote the use of more flexible and more efficient Table Drive Code Forms (TDCF), the CBS has decided to freeze the TACs, and complete a migration to TDCs by November 2014 for marine data, at which time the parallel international distribution of TAC and TDCF is to be stopped. The recommended TDCF for the distribution of time-critical maritime observations through the GTS is the BUFR code:

### FM 94–XIV BUFR - Binary universal form for the representation of meteorological data.

The status of the migration of the different TACs is given in Appendix A. Recognizing the deadline of November 2014 for the completion of the migration to TDCFs and the lack of operational BUFR templates for FM 18-XII, FM 64-XI and FM 65-XI and the timescales required for the validation and testing of new BUFR templates the following recommendation is made:

Recommendation 1: the team reviews the proposals for the CTD, moored and drifting buoy templates contained in Part B, the proposals for associated changes to the WMO Manual on Codes in Part C and comment and make decisions or recommendations as appropriate.

Whilst recognizing the origin of the GTS in the operational community and its role in the distribution of time-critical data it is noted that a number of delayed mode climate data streams are based on the data available from the GTS. In order to prevent discontinuities or data loss from the climate record through the migration to TCDFs the proposed templates have been designed to preserve information contained in the TACs.

Noting the above requirements from the climate community and recognizing that not all optional elements in the TACs have been fully used and that the transmission of large volumes of missing data will decrease the efficiency of the GTS the following recommendation is made:

Recommendation 2: The use of the optional elements in the BUFR templates should be monitored for a period of 2 years after which those elements that are not used can be recommended for removal.

Concerns of the climate community as noted by the JCOMM Expert Team on Marine Climatology (ETMC) and Ship Observations Team (SOT)

As noted above, a number of the delayed mode marine climate datasets (e.g. the International Comprehensive Ocean Atmosphere Data Set, ICOADS) are based on data extracted from the GTS. As a result, there has been concern within the community over the introduction of inhomogeneities and errors and the loss of data through the migration to TDCFs. This is based, in part, on a comparison of TAC and TDCF ship marine data where errors were detected in the BUFR data1. This is also based on a lack of familiarity with the TDCFs and the lack of human readability. The following recommendations are made to address these issues and are included in the proposals in part C. These recommendations are also include in an excerpt from the final report of the Seventh Session of the JCOMM Ship Observations Team (Appendix A).

Recommendation 3: For an initial period (a minimum of 2 years) an additional descriptor is included in the BUFR / CREX template for VOS reports giving the report in its original form before encoding into BUFR. This would require the addition of the following regulation to B/C 10 (and any update):

B/C 10.10	The element descriptor 2 05 YYY shall be included as the last element in all synoptic reports for sea stations, i.e. the data descriptors in Section 3 of the BUFR message for VOS shall be given by 3 08 009 2 05 YYY. The element 2 05 YYY shall include the synoptic report in its original form as reported and the YYY in the descriptor replaced by the number of characters in this element.

Recommendation 4: For an initial transition period of at least two years, the VOS reports shall also be distributed in parallel over the GTS in CREX as well as BUFR using the agreed BUFR / CREX template.

The JCOMM Expert Team on Marine Climatology, through its ad hoc group on data preservation, noted the possibility for ambiguity in the reporting of visual cloud reports from Voluntary Observing Ships caused by the observing in Oktas but reporting in whole %. To prevent this the following recommendation is made:

Recommendation 5: Update B/C 10 to reflect that cloud is typically observed in Oktas and give guidance on the coding of this in % by the addition of the following note to B/C 10.4.4.1:

2) When cloud cover is observed in Oktas the cloud cover shall be converted to percent, with fractional numbers rounded up (e.g. 1 Okta = 12.5%, rounded to 13 %).

The 7th Session of the JCOMM SOT (SOT-7) noted and concurred with a proposal from the UK Met Office for the “Surface Station Type” and “Generic Type of Humidity Instrument” to be added to the marine BUFR templates (See Appendix A). In response to this the following recommendations are made and proposed changes included in part C:

Recommendation 6: For templates in operational use the element “surface station type” should be included in the platform identification section of BUFR templates.

Recommendation 7: For marine reports containing humidity data the following two elements are proposed to be added to WMO Publication No 306 and to the ship temperature and humidity data table D sequence 3 02 053. This change is reflected in the proposals contained in the Part C.

It should be noted that Recommendation 7 has been modified slightly from the original request to the SOT to reflect the metadata collected for the ship observations through WMO Publication No 47.

Inclusion of Metadata in BUFR templates

The importance of reporting the metadata required to enable the real time interpretation of the observations has been recognized, as demonstrated in the template for meteorological observations from Voluntary Observing Ships (B/C 10, TM308009) and in the terms of reference for the JCOMM Task Team on Table Driven Code forms. Examples include the height at which the observations are made and the period over which data have been averaged for period, e.g. wind speed, precipitation etc. Whilst recognizing the importance of this metadata the JCOMM Data Buoy Cooperation Panel (DBCP) the proposed BUFR templates for moored buoys omitted this information in preference to providing the information via the JCOMM buoy metadata database, with end users associating the observations with metadata themselves. This preference is driven by the static nature of the metadata and a reluctance by the DBCP to transmit static data over the GTS. Noting

- that the buoy metadata database is not yet operational

- that the equivalent WMO database for VOS observations is ~ 3 years out of date

- the difficulty in associating the metadata with observations in the delayed mode data streams

and whilst recognising the concern of the DBCP the metadata required for the real time interpretation of the observations has been introduced to the templates proposed in this document. Based on this the following request / recommendation is made:

Recommendation 8: IPET-DRMM to advise the JCOMM Task Team on Table Driven Code forms and Data Buoy Cooperation Panel on best practices in relation to the inclusion of metadata in BUFR templates and the transmission of static data on the GTS.

PART B – PROPOSED BUFR TEMPLATES

B.1 Proposal for a new BUFR template for reporting Temperature, Salinity, Current and Depth Profile Data

B.1.1	Introduction

The template described in this proposal is designed to replace the current TESAC (FM64-Ext) message. In designing this template all elements of the current FM64-Ext message have been translated to prevent loss of data or the introduction of inhomogeneities by to the migration to TDCFs. A number of additional elements are also proposed – primarily metadata to enable the real time interpretation of the observations.

Where possible existing table D sequences have been used. Section B.1.2 describes the new proposed table D sequence for the profile data. Section B.1.3 maps the previous FM64-Ext elements to the proposed template.

B.1.2	Proposed new BUFR template for temperature, salinity and current profile data

Table B.1.1 defines the proposed BUFR template for temperature, salinity and current profile data.  Text in red indicates a new or modified element descriptor / table reference. Where new table references are defined the Y values have been set to Ynn. These new table references are defined Part C of this report and it has been left to the IPET-DRMM to specify the Y values for the new references.

Optional elements in the BUFR template have been specified through the use of short delayed descriptor replication factors to reduce the overhead when these elements are missing.

All temperatures are reported to 2 or more decimal places, i.e. 0.01 K, to prevent the loss of information on conversion between temperature units.

Table B.1.1: Sequence for the representation of temperature, salinity and current profile data (3 15 YY1)

| FXY | FXY | FXY | Meaning | Unit | Scale | Ref value | Data Width (bits) | Note |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3 15 YY1 |  |  | Sequence for representation of data derived from a ship based lowered instrument measuring subsurface seawater temperature, salinity and current profiles |  |  |  |  |  |
|  | 3 01 003 |  | Station identification and motion |  |  |  |  |  |
|  |  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 72 | 1 |
|  |  | 0 01 012 | Direction of motion of moving observing platform | degree true | 0 | 0 | 9 |  |
|  |  | 0 01 013 | Speed of motion of moving observing platform | m/s | 0 | 0 | 10 |  |
|  |  |  | Extended identification |  |  |  |  |  |
|  | 0 01 019 |  | Long Station or site name | CCITT IA5 | 0 | 0 | 256 | 2 |
|  | 0 01 103 |  | IMO Number. Unique Lloyd's registry. | Numeric | 0 | 0 | 24 | 3 |
|  | 0 01 087 |  | WMO Marine observing platform extended identifier | Numeric | 0 | 0 | 23 | 4 |
|  |  |  | Cruise / ship line information |  |  |  |  |  |
|  | 0 01 036 |  | Agency in charge of operating the observing platform | code table | 0 | 0 | 20 |  |
|  | 0 01 YY1 |  | Identifier of the cruise or mission under which the data were collected | CCITT IA5 | 0 | 0 | 160 | 5 |
|  | 0 01 080 |  | Ship line number according to SOOP | CCITT IA5 | 0 | 0 | 32 |  |
|  | 0 05 036 |  | Ship transect number according to SOOP | Numeric | 0 | 0 | 7 | 6 |
|  | 3 01 011 |  | Date |  |  |  |  |  |
|  |  | 0 04 001 | Year | a | 0 | 0 | 12 |  |
|  |  | 0 04 002 | Month | mon | 0 | 0 | 4 |  |
|  |  | 0 04 003 | Day | d | 0 | 0 | 6 |  |
|  | 3 01 012 |  | Time |  |  |  |  |  |
|  |  | 0 04 004 | Hour | h | 0 | 0 | 5 |  |
|  |  | 0 04 005 | Minute | min | 0 | 0 | 6 |  |
|  | 3 01 021 |  | Location (high accuracy) |  |  |  |  |  |
|  |  | 0 05 001 | Latitude (high accuracy) | deg | 5 | -9000000 | 25 |  |
|  |  | 0 06 001 | Longitude (high accuracy) | deg | 5 | -18000000 | 26 |  |
|  |  |  | Profile information |  |  |  |  |  |
|  | 0 01 079 |  | Unique identifier for the profile | CCITT IA5 | 0 | 0 | 64 | 7 |
|  | 0 01 023 |  | Observation sequence number | Numeric | 0 | 0 | 9 | 8 |
|  | 0 22 063 |  | Total depth of water | m | 0 | 0 | 14 |  |
|  |  |  | Surface pressure |  |  |  |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 9 |
|  | 3 02 001 |  | Pressure data |  |  |  |  |  |
|  |  | 0 10 004 | Pressure (at station level) | Pa | -1 | 0 | 14 |  |
|  |  | 0 10 051 | Pressure reduced to mean sea level | Pa | -1 | 0 | 14 |  |
|  |  | 0 10 061 | 3-hour pressure change | Pa | -1 | -500 | 10 |  |
|  |  | 0 10 063 | Characteristic of pressure tendency | Code table | 0 | 0 | 4 |  |
|  |  |  | Waves |  |  |  |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 9 |
|  | 3 02 021 |  | Waves |  |  |  |  |  |
|  |  | 0 22 001 | Direction of waves | degree true | 0 | 0 | 9 |  |
|  |  | 0 22 011 | Period of waves | s | 0 | 0 | 6 |  |
|  |  | 0 22 021 | Height of waves | m | 1 | 0 | 10 |  |
|  |  |  | Temperature and humidity data |  |  |  |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 9 |
|  | 3 02 052 |  | Temperature and humidity data |  |  |  |  |  |
|  |  | 0 07 032 | Height of sensor above marine deck platform (for temperature and humidity measurement) | m | 2 | 0 | 16 |  |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature and humidity measurement) | m | 0 | 0 | 12 |  |
|  |  | 0 12 101 | Temperature / air temperature | K | 2 | 0 | 16 |  |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table | 0 | 0 | 3 |  |
|  |  | 0 02 YY2 | Ventilation method for humidity sensor | Code table | 0 | 0 | 4 | 10 |
|  |  | 0 02 YY3 | Generic type of marine humidity sensor | Code table | 0 | 0 | 4 | 10 |
|  |  | 0 12 102 | Wet-bulb temperature | K | 2 | 0 | 16 |  |
|  |  | 0 12 103 | Dew-point temperature | K | 2 | 0 | 16 |  |
|  |  | 0 13 003 | Relative humidity | % | 0 | 0 | 7 |  |
|  |  |  | Wind data |  |  |  |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 9 |
|  | 3 02 059 |  | Ship wind data |  |  |  |  |  |
|  |  | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m | 2 | 0 | 16 |  |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m | 0 | 0 | 12 |  |
|  |  | 0 02 002 | Type of instrumentation for wind measurement | Flag table | 0 | 0 | 4 |  |
|  |  | 0 08 021 | Time significance (set = 2, time averaged) | Code table | 0 | 0 | 5 |  |
|  |  | 0 04 025 | Time period (= -10 minutes, or number of minutes after a significant change of wind) | min | 0 | -2048 | 12 |  |
|  |  | 0 11 001 | Wind direction | Degree true | 0 | 0 | 9 | 11,12 |
|  |  | 0 11 002 | Wind speed | m/s | 1 | 0 | 12 | 11,12 |
|  |  | 0 08 021 | Time significance (set to missing to cancel previous value) | Code table | 0 | 0 | 5 |  |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |  |  |  |  |
|  |  | 0 04 025 | Time period in minutes | min | 0 | -2048 | 12 | 13 |
|  |  | 0 11 043 | Maximum wind gust direction | degree true | 0 | 0 | 9 | 14 |
|  |  | 0 11 041 | Maximum wind gust speed | m/s | 1 | 0 | 12 | 14 |
|  |  |  | Surface Temperature, salinity and current |  |  |  |  |  |
|  | 0 22 067 |  | Instrument type for water temperature profile measurement | code table | 0 | 0 | 10 |  |
|  | 0 02 171 |  | Instrument serial number for water temperature / salinity profile measurement | CCITT IA5 | 0 | 0 | 64 | 15 |
|  | 3 02 090 |  | Surface temperature |  |  |  |  |  |
|  |  | 0 02 038 | Method of sea / water temperature measurement | Code table | 0 | 0 | 4 |  |
|  |  | 0 07 063 | Depth below sea / water surface (cm) | m | 2 | 0 | 20 |  |
|  |  | 0 22 045 | Sea / water temperature | K | 3 | 0 | 19 |  |
|  | 3 02 Y10 |  | Surface salinity |  |  |  |  |  |
|  |  | 0 02 033 | Method of sea / water salinity measurement | code table | 0 | 0 | 3 |  |
|  |  | 0 07 063 | Depth below sea / water surface (cm) | m | 2 | 0 | 20 |  |
|  |  | 0 22 064 | Salinity | ‰ | 3 | 0 | 17 |  |
|  | 3 02 Y11 |  | Surface current |  |  |  |  |  |
|  |  | 0 02 031 | Duration and time of current measurement | Code table | 0 | 0 | 5 |  |
|  |  | 0 02 YY4 | Method of sea / water current measurement | code table | 0 | 0 | 4 |  |
|  |  | 0 02 040 | Method of removing velocity and motion of platform from current | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 005 | Direction of sea surface current | Degree true | 0 | 0 | 9 |  |
|  |  | 0 22 032 | Speed of sea surface current | m/s | 2 | 0 | 13 |  |
|  | 0 02 171 |  | Instrument serial number for water temperature measurement (set to missing to cancel previous value) | CCITT IA5 | 0 | 0 | 64 |  |
|  | 0 22 067 |  | Instrument type for water temperature profile measurement (set to missing to cancel previous value) | code table | 0 | 0 | 10 |  |
|  |  |  | T & S profile data |  |  |  |  |  |
|  | 0 02 038 |  | Method of sea / water temperature measurement | Code table | 0 | 0 | 4 |  |
|  | 0 22 067 |  | Instrument type for water temperature profile measurement | Code table | 0 | 0 | 10 |  |
|  | 0 22 068 |  | Water temperature profile recorder type | Code table | 0 | 0 | 7 |  |
|  | 0 02 171 |  | Instrument serial number for water temperature measurement | CCITT IA5 | 0 | 0 | 64 | 15 |
|  | 0 02 033 |  | Method of sea / water salinity measurement | Code table | 0 | 0 | 3 |  |
|  | 0 02 032 |  | Indicator for digitization | Code table | 0 | 0 | 2 | 16 |
|  | 0 22 056 |  | Direction of profile | Code table | 0 | 0 | 2 | 17 |
|  | 0 02 YY5 |  | Method of depth calculation | Code table | 0 | 0 | 2 |  |
|  | 3 15 Y12 |  | Temperature and salinity profile |  |  |  |  |  |
|  |  | 1 12 000 | Delayed replication of 12 descriptors |  |  |  |  |  |
|  |  | 0 31 002 | Extended delayed replication factor | Numeric | 0 | 0 | 16 |  |
|  |  | 0 07 062 | Depth below sea / water surface (m) | m | 1 | 0 | 17 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 13, indicates depth at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 07 065 | Water pressure | Pa | -3 | 0 | 17 | 19 |
|  |  | 0 08 080 | Qualifier for quality class (set to 10, indicates water pressure at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 043 | Sea / water temperature | K | 2 | 0 | 15 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 11, indicates temperature at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 064 | Salinity | ‰ | 2 | 0 | 14 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 12, indicates salinity at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  |  | Current profile data |  |  |  |  |  |
|  | 1 06 000 |  | Delayed replication of 6 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 18 |
|  | 0 02 032 |  | Indicator for digitization | code table | 0 | 0 | 2 | 16 |
|  | 0 02 YY4 |  | Method of sea / water current measurement | code table | 0 | 0 | 4 |  |
|  | 0 02 031 |  | Duration and time of current measurement | code table | 0 | 0 | 5 |  |
|  | 0 02 040 |  | Method of removing velocity and motion of platform from current | Code table | 0 | 0 | 4 |  |
|  | 0 22 056 |  | Direction of profile | code table | 0 | 0 | 2 | 17 |
|  | 0 02 YY5 |  | Method of depth calculation | Code table | 0 | 0 | 2 |  |  |
|  | 3 15 Y13 |  | Current profile |  |  |  |  |  |
|  |  | 1 12 000 | Delayed replication of 12 descriptors |  |  |  |  |  |
|  |  | 0 31 002 | Extended delayed replication factor | Numeric | 0 | 0 | 16 |  |
|  |  | 0 07 062 | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 13, indicates depth at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 07 065 | Water pressure | Pa | -3 | 0 | 17 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 10, indicates water pressure at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 031 | Speed of current | m/s | 2 | 0 | 13 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 14, indicates current speed at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 004 | Direction of current | Degree true | 0 | 0 | 9 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 15, indicates current direction at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  |  | Dissolved oxygen profile data |  |  |  |  |  |
|  | 1 06 000 |  | Delayed replication of 4 descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed replication factor | Numeric | 0 | 0 | 1 | 18 |
|  | 0 02 032 |  | Indicator for digitization | code table | 0 | 0 | 2 | 16 |
|  | 0 02 Y21 |  | Instrument type / sensor for dissolved oxygen measurement | code table | 0 | 0 | 4 |  |
|  | 0 02 YY5 |  | Method of depth calculation | code table | 0 | 0 | 2 |  |
|  | 3 15 Y23 |  | Dissolved oxygen profile |  |  |  |  |  |
|  |  | 1 09 000 | Delayed replication of 9 descriptors |  |  |  |  |  |
|  |  | 0 31 002 | Extended delayed descriptor replication factor | Numeric | 0 | 0 | 16 |  |
|  |  | 0 07 062 | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 13, indicates depth at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 07 065 | Water pressure | Pa | -3 | 0 | 17 | 19 |
|  |  | 0 08 080 | Qualifier for quality class (set to 10, indicates water pressure at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |
|  |  | 0 22 Y22 | Dissolved oxygen | mol kg-1 | 3 | 0 | 19 |  |
|  |  | 0 08 080 | Qualifier for quality class (set to 16, indicates dissolved oxygen at a level) | Code table | 0 | 0 | 6 |  |
|  |  | 0 33 050 | GTSPP quality class | Code table | 0 | 0 | 4 |  |

Notes:

- Place the ship call sign here.

- Place the ship name here.

- Values are restricted to between 0 and 9999999.

- If field 0-01-011 is used (ship call sign) this field will be left missing and vice versa.

- Place the cruise identifier here, set to missing if no cruise identifier has been set.

- Integer, assigned by the operator, incremented for each new transect (i.e. all drops have the same transect number while the ship is moving from one end point of the line to the other end point; as soon as the ship arrived to port and goes back to start a new transect then transect number is incremented). The initial value and subsequent values for transect numbers do not matter provided that each new transect by a ship on a line has a transect number higher than previous transect numbers for the same line and the same ship. In case a single cruise follows more than one SOOP line in a row, then the transect number should be incremented each time the cruise changes line.

- Currently some countries use a 32 bit CRC calculation to generate a unique identifier for the individual TESAC messages. This corresponds to a 8-octet long hexadecimal string.

- Enter the cast / station number along the line / transect here.

- When the following optional data are included in the report this shall be set to 1, zero otherwise.

- The type of humidity sensor and method of ventilation shall be coded here. Where this information is unavailable these fields shall be set to missing.

- The mean direction and speed of the wind over the 10-minute period immediately preceding the observation shall be reported. The time period (0 04 025) shall be included as -10. However, when the 10-minute period includes a discontinuity in the wind characteristics, only data obtained after the discontinuity shall be used for reporting the mean values, and hence the period (0 04 025) in these circumstances shall be correspondingly reduced.

- The time period is preceded by a time significance qualifier (0 08 021) that shall be set to 2 (Time averaged).

  - The wind direction (0 11 001) shall be reported in degrees true and the wind speed (0 11 002) shall be reported in meters per second (with precision in tenths of a meter per second).

  - In the absence of wind instruments, the wind speed shall be estimated on the basis of the Beaufort wind scale. The Beaufort number obtained by estimation is converted into meters per second by use of the wind speed equivalent columns on the Beaufort scale, and this speed is reported for wind speed.

- Time period for maximum wind gust direction and speed (0 04 025) shall be determined by regional or national decision and reported as a negative value in minutes.

- Direction of the maximum wind gust (0 11 043) shall be reported in degrees true and speed of the maximum wind gust (0 11 041) shall be reported in meters per second (with precision in tenths of meters per second).

- Insert the serial number for the CTD used to make profile measurement. Where the serial number is longer than 8 characters enter the last 8 characters.

- This descriptor applies to the method used to select depths for all of the profiles encoded. If values are reported at signiﬁcant depths, the values shall: 
(a) be sufficient to reproduce basic features of the proﬁle and; 
(b) deﬁne the top and the bottom of isothermal and isopycnal layers.

- This descriptor indicates the direction for the profile sampling.

- When current / dissolved oxygen data are included in the report this shall be set to 1, zero otherwise.

- When pressure is recorded this value shall be set otherwise this value shall be set to missing.

B.1.3	Mapping of TESAC (FM-64) to BUFR template

|  | Name / description | BUFR mapping | Notes / comments |
| --- | --- | --- | --- |
| Section 1 | MiMiMjMj YYMMJ GGgg/ QcLaLaLaLaLa LoLoLoLoLoLo (iuddff) (4snTTT) |
| MiMi | Identification letters of the report | N/A |  |
| MjMj | Identification letters of the part of the report or the version of the code form | N/A |  |
| YY | Day of the month (UTC) on which the actual time of the observation falls | 0 04 003 |  |
| MM | Month of the year (UTC) | 0 04 002 |  |
| J | Units digit of the year | 0 04 001 | Full year in BUFR rather than last digit |
| GGgg | Time in hours (GG) and minutes (gg) UTC of launching the bathythermograph | 0 04 004 0 04 005 | Time of launching BT not specified – add as regulation |
| Qc | Quadrant of the globe | N/A | Sign included in BUFR location, Qc not needed |
| LaLaLaLaLa | Latitude, in thousands of a degree (3 d.p.) | 0 05 001 | 5 d.p. in BUFR |
| LoLoLoLoLoLo | Longitude, in thousands of a degree (3 d.p.) | 0 06 001 | 5 d.p. in BUFR |
| iu | Indicator for units of wind speed and instrumentation | 0 02 002 |  |
| dd | True direction, in tens of degrees, from which wind is blowing | 0 11 001 | To nearest degree in BUFR |
| ff | Wind speed in units indicated by iu | 0 11 002 | 1 d.p. in BUFR |
| sn | Sign of the data | N/A | Sign included in BUFR value |
| TTT | Air temperature in tenths of a degree C | 0 12 101 | K, 2 d.p. in BUFR |
| Section 2 | 888k1k2 IXIXIXXRXR 2z0z0z0z0 3T0T0T0T0 4S0S0S0S0 … 2znznznzn 3TnTnTnTn 4SnSnSnSn (00000) |
| k1 | Indicator for digitisation | 0 02 032 |  |
| k2 | Method of salinity / depth measurement | 0 02 033 |  |
| IXIXIX | Instrument type for XBT with fall rate equation coefficients | 0 22 067 |  |
| XRXR | Recorder type | 0 22 068 |  |
| z0z0z0z0 | Selected and/or significant depths (m) starting with the surface | 0 07 062 |  |
| T0T0T0T0 | Temperature in hundredths of degrees C | 0 22 043 | K, 2 d.p. |
| S0S0S0S0 | Salinity in hundredths of a part per thousand | 0 22 064 |  |
| 00000 | Indicator that last value is for bottom layer of ocean |  |  |
| Section 3 | 66k6k4k3 2z0z0z0z0 d0d0c0c0c0 … 2znznznzn dndncncncn |
| 66 | N/A |  |  |
| k6 | Method of removing the velocity and motion of the ship or buoy from current measurement | 0 02 040 |  |
| k4 | Period of current measurement (drift method) | 0 02 031 |  |
| k3 | Duration and time of current measurement | 0 02 031 |  |
| zozozozo | Depth | 0 07 062 |  |
| d0d0 | True direction in tens of degrees towards which the sea current is moving | 0 22 004 | Nearest degree |
| c0c0c0 | Speed of the current in cm/s | 0 22 031 | m/s, 2 d.p. |
| Section 4 | 55555 1ZdZdZdZd |
| ZdZdZdZd | total depth | 0 22 063 |  |
| Section 5 | D…D or 99999 A1bwnbnbnb |
| D…D | Callsign | 0 01 011 |  |
| A1bwnbnbnb | Buoy Id | 0 01 087 |  |

B.2 Proposed BUFR template for the reporting of moored buoy data

Table B.2.1 gives the expanded BUFR template for the reporting of moored buoy data. This template is designed towards meeting the flexibility of a minimum number of cohesive common descriptors which can be grouped together so avoiding a long common sequence that requires a higher bandwidth for data transmission (and may contain many unused elements).

As with the template for temperature, salinity and current profile data, the optional sequences are defined through the use of delayed replication factors.

All temperatures are encoded to 2 or more decimal places. The sea (surface) temperatures can be reported to either 0.1 K or 0.01 K precision according to the accuracy of the sensor. To indicate this accuracy the use of the "precision of temperature observation" descriptor (0 02 005) has been used.

Some moorings record both sub-surface salinity and temperature measurements, others just the temperature. To accommodate this optional sequences for only sub-surface temperatures and sub-surface temperature and salinity are included.

Text in red indicates new or modified descriptors. These are described in Part C of this report.

Table B.2.1: Sequence for the representation of data from moored buoys

| FXY | FXY | FXY | Meaning | Unit | Scale | Ref value | Data Width (bits) | Note |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Template for moored buoy data |  |  |  |  |  |
|  |  |  | Buoy identification and location |  |  |  |  |  |
| 3 01 Y14 |  |  | Sequence for representation of moored buoy identification |  |  |  |  |  |
|  | 0 01 087 |  | WMO marine observing platform extended identifier | Numeric | 0 | 0 | 23 |  |
|  | 0 01 015 |  | Station or site name | CCITT IA5 | 0 | 0 | 160 |  |
|  | 0 02 149 |  | Type of data buoy | Code table | 0 | 0 | 6 |  |
|  |  |  | Date and time |  |  |  |  |  |
|  | 3 01 011 |  | Date |  |  |  |  |  |
|  |  | 0 04 001 | Year | a | 0 | 0 | 12 |  |
|  |  | 0 04 002 | Month | mon | 0 | 0 | 4 |  |
|  |  | 0 04 003 | Day | d | 0 | 0 | 6 |  |
|  | 3 01 012 |  | Time |  |  |  |  |  |
|  |  | 0 04 004 | Hour | h | 0 | 0 | 5 |  |
|  |  | 0 04 005 | Minute | min | 0 | 0 | 6 |  |
|  |  |  | Location |  |  |  |  |  |
|  | 3 01 021 |  | Location (high accuracy) |  |  |  |  |  |
|  |  | 0 05 001 | Latitude (high accuracy) | ° | 5 | -9000000 | 25 |  |
|  |  | 0 06 001 | Longitude (high accuracy) | ° | 5 | -18000000 | 26 |  |
|  |  |  | Standard meteorological data |  |  |  |  |  |
| 3 02 Y15 |  |  | Sequence for representation of standard surface marine meteorological measurements from moored buoys |  |  |  |  |  |
|  | 0 10 004 |  | Pressure | Pa | -1 | 0 | 14 |  |
|  | 0 10 051 |  | Pressure reduced to mean sea level | Pa | -1 | 0 | 14 |  |
|  | 0 07 033 |  | Height of sensor above water surface | m | 1 | 0 | 12 |  |
|  | 0 12 101 |  | Temperature / air temperature | K | 2 | 0 | 16 |  |
|  | 0 12 103 |  | Dew point temperature | K | 2 | 0 | 16 |  |
|  | 0 13 003 |  | Relative humidity | % | 0 | 0 | 7 |  |
|  | 0 07 033 |  | Height of sensor above water surface | m | 1 | 0 | 12 | 1 |
|  | 0 08 021 |  | Time significance (=2, time average) | Code table | 0 | 0 | 5 |  |
|  | 0 04 025 |  | Time period or displacement | min | 0 | -2048 | 12 |  |
|  | 0 11 001 |  | Wind direction | degree true | 0 | 0 | 9 |  |
|  | 0 11 002 |  | Wind speed | m s-1 | 1 | 0 | 12 |  |
|  | 0 08 021 |  | Time significance (set to missing to cancel previous value) | Code table | 0 | 0 | 5 |  |
|  | 0 04 025 |  | Time period or displacement | min | 0 | -2048 | 12 |  |
|  | 0 11 041 |  | Maximum gust speed | m s-1 | 1 | 0 | 12 |  |
|  | 0 04 025 |  | Time period or displacement (set to missing) | min | 0 | -2048 | 12 |  |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel previous value) | m | 1 | 0 | 12 |  |
|  | 0 02 005 |  | Precision of temperature | K | 2 | 0 | 7 |  |
|  | 0 07 063 |  | Depth below sea / water surface (cm) | m | 2 | 0 | 20 |  |
|  | 0 22 049 |  | Sea-surface temperature | K | 2 | 0 | 15 |  |
|  |  |  | Optional ancillary met data |  |  |  |  |  |
| 1 01 000 |  |  | Replicate next sequence |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 3 02 Y16 |  |  | Sequence for representation of ancillary meteorological observations |  |  |  |  |  |
|  | 0 20 001 |  | Horizontal visibility | m | -1 | 0 | 13 |  |
|  | 0 04 024 |  | Time period or displacement | h | 0 | -2048 | 12 |  |
|  | 0 13 011 |  | Total precipitation / total water equivalent | kg m-2 | 1 | -1 | 14 |  |
|  |  |  | Optional radiation measurements |  |  |  |  |  |
| 1 01 000 |  |  | Replicate next sequence |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 3 02 082 |  |  | Sequence for representation of radiation measurements |  |  |  |  |  |
|  | 0 04 025 |  | Time period or displacement | min | 0 | -2048 | 12 |  |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified | J m-2 | -3 | -65536 | 17 |  |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified | J m-2 | -3 | -65536 | 17 |  |
|  | 0 14 016 |  | Net radiation, integrated over period specified | J m-2 | -4 | -16384 | 15 |  |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 |  |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 |  |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 |  |
|  |  |  | Optional basic wave measurements |  |  |  |  |  |
| 1 01 000 |  |  | Replicate next sequence |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 3 02 Y17 |  |  | Sequence for representation of basic wave measurements |  |  |  |  |  |
|  | 0 22 078 |  | Duration of wave record | s | 0 | 0 | 12 | 3 |
|  | 0 22 070 |  | Significant wave height | m | 2 | 0 | 13 |  |
|  | 0 22 073 |  | Maximum wave height | m | 2 | 0 | 13 |  |
|  | 0 22 074 |  | Average wave period | s | 1 | 0 | 9 |  |
|  | 0 22 071 |  | Spectral peak wave period | s | 1 | 0 | 9 |  |
|  | 0 22 076 |  | Direction from which dominant waves are coming | degree true | 0 | 0 | 9 |  |
|  | 0 22 077 |  | Directional spread of dominant wave | ° | 0 | 0 | 9 |  |
|  |  |  | Optional spectral wave measurements |  |  |  |  |  |
| 1 01 000 |  |  | Replicate next sequence |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 3 02 Y18 |  |  | Sequence for representation of detailed spectral wave measurements |  |  |  |  |  |
|  | 0 22 078 |  | Duration of wave record | s | 0 | 0 | 12 | 3 |
|  | 0 22 082 |  | Maximum non-directional spectral wave density | m2 s | 2 | 0 | 20 |  |
|  | 1 06 000 |  | Replicate 6 descriptors |  |  |  |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 | 4 |
|  | 0 22 080 |  | Waveband central frequency | Hz | 3 | 0 | 10 |  |
|  | 0 22 069 |  | Spectral wave density | m2 Hz-1 | 3 | 0 | 22 |  |
|  | 0 22 086 |  | Mean direction from which waves are coming | degree true | 0 | 0 | 9 |  |
|  | 0 22 087 |  | Principle direction from which waves are coming | degree true | 0 | 0 | 9 |  |
|  | 0 22 088 |  | First normalized polar coordinate from Fourier coefficients | Numeric | 2 | 0 | 7 |  |
|  | 0 22 089 |  | Second normalized polar coordinate from Fourier coefficients | Numeric | 2 | 0 | 7 |  |
|  |  |  | Optional temperature profile measurements |  |  |  |  |  |
| 1 02 000 |  |  | Replicate next 2 sequences |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 0 02 005 |  |  | Precision of temperature observation | K | 2 | 0 | 7 |  |
| 3 06 Y19 |  |  | Depth and temperature profile (high accuracy) |  |  |  |  |  |
|  | 0 02 032 |  | Indicator for digitization | Code table | 0 | 0 | 2 |  |
|  | 1 02 000 |  | Delayed replication for 2 descriptors |  |  |  |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |  |
|  | 0 07 062 |  | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  | 0 22 043 |  | Sea / water temperature | K | 2 | 0 | 15 |  |
|  |  |  | Optional temperature and salinity profile measurements |  |  |  |  |  |
| 1 02 000 |  |  | Replicate next 2 sequences |  |  |  |  |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 2 |
| 0 02 005 |  |  | Precision of temperature observation | K | 2 | 0 | 7 |  |
| 3 06 004 |  |  | Depth, temperature and salinity profile |  |  |  |  |  |
|  | 0 02 032 |  | Indicator for digitization | Code table | 0 | 0 | 2 |  |
|  | 0 02 033 |  | Method of salinity / depth measurement | Code table | 0 | 0 | 3 |  |
|  | 1 03 000 |  | Delayed replication for 3 descriptors |  |  |  |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |  |
|  | 0 07 062 |  | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  | 0 22 043 |  | Sea / water temperature | K | 2 | 0 | 15 |  |
|  | 0 22 062 |  | Salinity | ‰ | 2 | 0 | 14 |  |
|  |  |  | Optional sub-surface current measurements |  |  |  |  |  |
| 1 01 000 |  |  | Replicate next sequence | Numeric | 0 | 0 | 1 |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor |  |  |  |  | 2 |
| 3 06 005 |  |  | Sequence for representation of sub-surface current measurements |  |  |  |  |  |
|  | 0 02 031 |  | Duration and time of current measurement | Code table | 0 | 0 | 5 |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptors |  |  |  |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |  |
|  | 0 07 062 |  | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  | 0 22 004 |  | Direction of current | degree true | 0 | 0 | 9 |  |
|  | 0 22 031 |  | Speed of current | m s-1 | 2 | 0 | 13 |  |

Notes

- For buoys equipped with more than 1 anemometer this height should relate to the one being used.

- In data 0 to skip next descriptors, 1 to use

- Length of wave sampling period

- Number of frequency bins

B.3 Proposed BUFR template for the reporting of drifting buoy template

The proposed BUFR template for drifting buoys is given in Table B.3.1. The template is based on that currently used for drifters (under validation) but with the descriptors relevant to only moored buoys omitted. A number of other descriptors that are no longer needed, as we know a priori from the template descriptor that this is a drifter, have also been omitted.

The proposed template is appropriate for SVP and SVP-B drifters that form the backbone of the global drifter array. Additional expanded descriptors (sequences) can be used for drifters that have salinity sensors, wind measurements and thermistor chains. If these are not present then the replication factor that precedes each sequence should be coded as 0 in the data string to skip that sequence. Similarly an optional sequence for basic wave measurements is included, anticipating future capability. The template is also applicable for ice buoys (whether drifters or beacons deployed on the ice or ice-mass balance buoys).

Table B.3.1: Proposed BUFR template for the representation of drifting buoy data

| FXY | FXY | FXY | Meaning | Unit | Scale | Ref value | Data Width (bits) | Note |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Template for drifting buoy data |  |  |  |  |  |
|  | 0 01 087 |  | WMO marine observing platform extended identifier | Numeric | 0 | 0 | 23 |  |
|  | 0 01 019 |  | Long station name | CCITT IA5 | 0 | 0 | 256 |  |
|  | 0 02 149 |  | Type of data buoy | Code table | 0 | 0 | 6 |  |
|  |  |  | Time / date of last known position |  |  |  |  |  |
|  | 0 08 021 |  | Time significance (set to 26, time of last known position) | Code table | 0 | 0 | 5 |  |
|  | 3 01 011 |  | Date |  |  |  |  | 1 |
|  |  | 0 04 001 | Year | a | 0 | 0 | 12 |  |
|  |  | 0 04 002 | Month | mon | 0 | 0 | 4 |  |
|  |  | 0 04 003 | Day | d | 0 | 0 | 6 |  |
|  | 3 01 012 |  | Time |  |  |  |  | 2 |
|  |  | 0 04 004 | Hour | h | 0 | 0 | 5 |  |
|  |  | 0 04 005 | Minute | min | 0 | 0 | 6 |  |
|  |  |  | Location and location quality |  |  |  |  |  |
|  | 3 01 021 |  | Latitude and Longitude (high accuracy) |  |  |  |  |  |
|  |  | 0 05 001 | Latitude (high accuracy) | ° | 5 | -9000000 | 25 |  |
|  |  | 0 06 001 | Longitude (high accuracy) | ° | 5 | -18000000 | 26 |  |
|  | 2 08 016 |  | Change width of CCITT IA5 field (change to 16 characters) |  |  |  |  |  |
|  | 0 01 051 |  | Platform Transmitter ID number | CCITT IA5 | 0 | 0 | 128 | 3 |
|  | 2 08 000 |  | Change data width (cancel previous value) |  |  |  |  |  |
|  | 0 02 148 |  | Data collection and / or location system | Code table | 0 | 0 | 5 | 4 |
|  | 0 01 012 |  | Direction of motion of moving observing platform | degree true | 0 | 0 | 9 | 5 |
|  | 0 01 014 |  | Speed of motion of moving observing platform | m s-1 | 0 | 0 | 10 | 6 |
|  | 0 33 022 |  | Quality of buoy satellite transmission | Code table | 0 | 0 | 2 | 7 |
|  | 0 33 023 |  | Quality of buoy location | Code table | 0 | 0 | 2 | 8 |
|  | 0 33 027 |  | Location quality class (range of radius of 66% confidence) | Code table | 0 | 0 | 3 | 9 |
|  | 0 25 026 |  | Battery voltage (large range) | V | 1 | 0 | 12 | 10 |
|  |  |  | Drogue status |  |  |  |  |  |
|  | 0 02 034 |  | Drogue type | Code table | 0 | 0 | 5 |  |
|  | 0 22 060 |  | Lagrangian drifter drogue status | Code table | 0 | 0 | 3 |  |
|  | 0 07 070 |  | Drogue depth | m | 0 | 0 | 10 |  |
|  | 0 02 190 |  | Lagrangian drifter submergence | % | 0 | 0 | 7 | 11 |
|  |  |  | Time / date of observation |  |  |  |  |  |
|  | 0 08 021 |  | Time significance (set to 25, nominal reporting time) | Code table | 0 | 0 | 5 |  |
|  | 3 01 011 |  | Date |  |  |  |  | 12 |
|  |  | 0 04 001 | Year | a | 0 | 0 | 12 |  |
|  |  | 0 04 002 | Month | mon | 0 | 0 | 4 |  |
|  |  | 0 04 003 | Day | d | 0 | 0 | 6 |  |
|  | 3 01 012 |  | Time |  |  |  |  | 13 |
|  |  | 0 04 004 | Hour | h | 0 | 0 | 5 |  |
|  |  | 0 04 005 | Minute | min | 0 | 0 | 6 |  |
|  |  |  | Surface temperature and salinity |  |  |  |  |  |
|  | 0 02 005 |  | Precision of temperature observation | K | 2 | 0 | 7 |  |
|  | 0 22 043 |  | Sea / water temperature | K | 2 | 0 | 15 |  |
|  | 0 02 033 |  | Method of salinity / depth measurement | Code table | 0 | 0 | 3 | 14 |
|  | 0 22 059 |  | Sea-surface salinity | ‰ | 2 | 0 | 14 |  |
|  |  |  | Surface type / ice information |  |  |  |  |  |
|  | 0 08 029 |  | Surface type | Code table | 0 | 0 | 8 |  |
|  | 0 13 115 |  | Ice thickness | m | 2 | 0 | 19 |  |
|  |  |  | Optional temperature and salinity profile measurements |  |  |  |  |  |
|  | 1 03 000 |  | Replicate next 3 sequences |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 15 |
|  | 0 02 005 |  | Precision of temperature observation | K | 2 | 0 | 7 |  |  |
|  | 3 06 004 |  | Depth, temperature and salinity profile |  |  |  |  |  |
|  |  | 0 02 032 | Indicator for digitization | Code table | 0 | 0 | 2 |  |
|  |  | 0 02 033 | Method of salinity / depth measurement | Code table | 0 | 0 | 3 |  |
|  |  | 1 03 000 | Delayed replication of 3 elements |  |  |  |  |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |  |
|  |  | 0 07 062 | Depth below sea / water surface | m | 1 | 0 | 17 |  |
|  |  | 0 22 043 | Sea / water temperature | K | 2 | 0 | 15 |  |
|  |  | 0 22 062 | Salinity | ‰ | 2 | 0 | 14 |  |
|  | 0 02 005 |  | Precision of temperature observation (set to missing to cancel previous value) | K | 2 | 0 | 7 |  |
|  |  |  | Pressure and air temperature data |  |  |  |  |  |
|  | 0 10 004 |  | Pressure | Pa | -1 | 0 | 14 |  |
|  | 0 10 051 |  | Pressure reduced to mean sea level | Pa | -1 | 0 | 14 |  |
|  | 1 02 000 |  | Replicate next two descriptors |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 15 |
|  | 0 07 033 |  | Height of sensor above water surface | m | 1 | 0 | 12 |  |
|  | 0 12 101 |  | Temperature / air temperature | K | 2 | 0 | 16 |  |
|  |  |  | Wind data |  |  |  |  |  |
|  | 1 01 000 |  | Replicate next sequence |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 15 |
|  | 3 02 Y20 |  | Wind measurement from drifting buoy |  |  |  |  |  |
|  |  | 0 02 169 | Anemometer type | Code table | 0 | 0 | 4 | 16 |
|  |  | 0 07 033 | Height of sensor above water surface | m | 1 | 0 | 12 | 17 |
|  |  | 0 08 021 | Time significance | Code table | 0 | 0 | 5 | 18 |
|  |  | 0 04 025 | Time period or displacement | min | 0 | -2048 | 12 | 19 |
|  |  | 0 11 001 | Wind direction | degree true | 0 | 0 | 9 | 20 |
|  |  | 0 11 002 | Wind speed | m s-1 | 0 | 0 | 12 | 20 |
|  |  |  | Wave data |  |  |  |  |  |
|  | 1 01 000 |  | Repeat next sequence |  |  |  |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric | 0 | 0 | 1 | 15 |
|  | 3 02 Y17 |  | Basic wave measurements |  |  |  |  |  |
|  |  | 0 22 078 | Duration of wave record | s | 0 | 0 | 12 | 21 |
|  |  | 0 22 070 | Significant wave height | m | 2 | 0 | 13 |  |
|  |  | 0 22 073 | Maximum wave height | m | 2 | 0 | 13 |  |
|  |  | 0 22 074 | Average wave period | s | 1 | 0 | 9 |  |
|  |  | 0 22 071 | Spectral peak wave period | s | 1 | 0 | 9 |  |
|  |  | 0 22 076 | Direction in which dominant waves are from | degree true | 0 | 0 | 9 |  |
|  |  | 0 22 077 | Directional spread of dominant wave | ° | 0 | 0 | 9 |  |

Notes:

- Date of last known position coded here

- Time of last known position coded here

- If Argos is used, Argos ID number; If Iridium used, Iridium IMEI number.

- 1 = Argos; 8 = Iridium & GPS; 9=Argos3

- Platform drift direction

- Platform drift speed

- 0 = Good; 1 = Dubious; 3 = missing

- 0 = Reliable; 1 = Last known position; 2 = Dubious; 3 = missing

- 0: ≥ 1500m; 1: ≥500m to <1500m; 2: ≥250m to <500m; 3: ≥100m to <250m; 4: <100m (new value); 7=missing

- Platform battery voltage

- % time submerged

- Date of observation

- Time of observation

- 0 = No salinity measured; 1 = In situ sensor, accuracy better than 0.02 ‰; 2 = In situ sensor, accuracy less than 0.02 ‰.

- In data 0 to skip next descriptors, 1 to use

- e.g. 2 = WOTAN; 3 = sonic anemometer

- Anemometer height or effective height for WOTAN

- Set = 2, time averaged

- Time in minutes

- At measurement height

- Length of wave sampling period

PART C – PROPOSED CHANGES TO DESCRIPTORS AND SEQUENCES

This section of the report includes the proposed changes to the WMO manual on codes required to accommodate the above proposed BUFR templates.

C.1 - Proposed new descriptors

| Table Reference | Element name | Unit | Scale | Ref. Value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
| 0 01 YY1 | Identifier of the cruise or mission under which the data were collected. | CCITT IA5 | 0 | 0 | 160 |
| 0 02 YY2 | Ventilation of humidity sensor | code table | 0 | 0 | 4 |
| 0 02 YY3 | Generic type of marine humidity sensor | code table | 0 | 0 | 4 |
| 0 02 YY4 | Method of sea / water current measurement | code table | 0 | 0 | 4 |
| 0 02 YY5 | Method of depth calculation | code table | 0 | 0 | 2 |
| F XX YY6 | Encryption method used | code table | 0 | 0 | 8 |
| F XX YY7 | Encryption key version | code table | 0 | 0 | 16 |
| 0 01 YY8 | Encrypted ship or mobile land station identifier Ship's call sign | Binary | 0 | 0 | 256 |
| F XX YY9 | Surface station type | Code table | 0 | 0 | 4 |
| 0 02 Y21 | Instrument type / sensor for dissolved oxygen measurement | Code table | 0 | 0 | 4 |
| 0 22 Y22 | Dissolved oxygen | mol kg-1 | 3 | 0 | 19 |

C.2 Proposed modifications to descriptors

| Table Reference | Element name | Unit | Scale | Ref. Value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
| 0 22 067 | Instrument type for water temperature / salinity profile measurement | code table | 0 | 0 | 10 |

The modification to this descriptor is highlighted in red. This has been expanded to include the type of salinity profile measurement for use in the CTD template.

C.3 Proposed new sequences

3 02 Y10

Surface salinity

| Table Reference | Table References | Element Name | Element description |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y10 | 0 | 02 | 033 | Method of sea / water salinity measurement |  |
|  | 0 | 07 | 063 | Depth below sea / water surface (cm) |  |
|  | 0 | 22 | 064 | Salinity |  |

This sequence is required to represent the surface salinity in the CTD template.

3 02 Y11

Surface current

| Table Reference | Table References | Element Name | Element description |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y11 | 0 | 02 | 031 | Duration and time of current measurement |  |
|  |  |  | 0 | 02 | YY6 | Method of sea / water current measurement |  |
|  | 0 | 02 | 040 | Method of removing velocity and motion of platform from current |  |
|  | 0 | 22 | 005 | Direction of sea surface current |  |
|  | 0 | 22 | 032 | Speed of sea surface current |  |

This template is required to represent the surface current in the CTD template.

3 15 Y12

Temperature and salinity profile

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 15 | Y12 | 1 | 12 | 000 | Delayed replication of 12 descriptors |  |
|  | 0 | 31 | 002 | Extended delayed replication factor |  |
|  | 0 | 07 | 062 | Depth below sea / water surface (m) |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 13, indicates depth at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 07 | 065 | Water pressure |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 10, indicates pressure at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 22 | 043 | Sea / water temperature |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 11, indicates temperature at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 22 | 064 | Salinity | Set to 12, indicates salinity at a level |
|  | 0 | 08 | 080 | Qualifier for quality class |  |
|  | 0 | 33 | 050 | GTSPP quality class |  |

This sequence is required for the representation of the temperature and salinity profile data in the CTD template. This differs from 3 06 004 through the inclusion of pressure (the observed variable) and depth and through the inclusion of the required quality flags.

3 15 Y13

Current profile

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 15 | Y13 | 1 | 12 | 000 | Delayed replication of 12 descriptors |  |
|  | 0 | 31 | 002 | Extended delayed replication factor |  |
|  | 0 | 07 | 062 | Depth below sea / water surface (m) |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 13, indicates depth at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 07 | 065 | Water pressure |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 10, indicates pressure at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 22 | 031 | Speed of current |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 14, indicates current speed at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 22 | 004 | Direction of current |  |
|  | 0 | 08 | 080 | Qualifier for quality class | Set to 15, indicates current direction at a level |
|  | 0 | 33 | 050 | GTSPP quality class |  |

This sequence is required for the representation of current profile data in the CTD template.

3 01 Y14

Sequence for representation of moored buoy identification

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 01 | Y14 |  |  |  | Sequence for representation of moored buoy identification |  |
|  | 0 | 01 | 087 | WMO marine observing platform extended identifier |  |
|  | 0 | 01 | 015 | Station or site name |  |
|  | 0 | 02 | 149 | Type of data buoy |  |
|  | 3 | 01 | 011 | Date |  |
|  | 3 | 01 | 012 | Time |  |
|  | 3 | 01 | 021 | Location (high accuracy) |  |

This sequence is required for the representation of the moored buoy identification data in the moored buoy template.

3 02 Y15

Sequence for representation of standard surface marine meteorological observations from moored buoys

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y15 |  |  |  | Sequence for representation of standard surface marine meteorological observations from moored buoys |  |
|  | 0 | 10 | 004 | Pressure |  |
|  | 0 | 10 | 051 | Pressure reduced to mean sea level |  |
|  | 0 | 07 | 033 | Height of sensor above water surface | Height of air temperature / humidity sensor |
|  | 0 | 12 | 101 | Temperature / air temperature | At observation height |
|  | 0 | 12 | 103 | Dew point temperature | At observation height |
|  | 0 | 13 | 003 | Relative humidity | With respect to water at all temperatures |
|  | 0 | 07 | 033 | Height of sensor above water surface | Height of wind speed sensor |
|  | 0 | 08 | 021 | Time significance | =2, time average |
|  | 0 | 04 | 025 | Time period or displacement | Period over which winds are averaged |
|  | 0 | 11 | 001 | Wind direction | At observation height |
|  | 0 | 11 | 002 | Wind speed | At observation height |
|  | 0 | 08 | 021 | Time significance | Set to missing to cancel previous value |
|  | 0 | 04 | 025 | Time period or displacement | Time period over which maximum gust observed |
|  | 0 | 11 | 041 | Maximum gust speed |  |
|  | 0 | 04 | 025 | Time period or displacement | Set to missing to cancel previous value |
|  | 0 | 07 | 033 | Height of sensor above water surface | Set to missing to cancel previous value |
|  | 0 | 02 | 005 | Precision of temperature |  |
|  | 0 | 07 | 063 | Depth below sea / water surface |  |
|  | 0 | 22 | 049 | Sea-surface temperature |  |

This sequence is required for the representation of standard meteorological observations from moored buoys.  The instrument heights are required due to the use of instruments at non-standard measurement heights.

3 02 Y16

Sequence for representation of ancillary meteorological observations

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y16 |  |  |  | Sequence for representation of ancillary meteorological observations |  |
|  | 0 | 20 | 001 | Horizontal visibility |  |
|  | 0 | 04 | 024 | Time period or displacement |  |
|  | 0 | 13 | 011 | Total precipitation / total water equivalent |  |

This sequence is required for the (optional) reporting of visibility and precipitation from moored buoys.

3 02 Y17

Sequence for representation of basic wave measurements

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y17 |  |  |  | Sequence for representation of basic wave measurements |  |
|  | 0 | 22 | 078 | Duration of wave record |  |
|  | 0 | 22 | 070 | Significant wave height |  |
|  | 0 | 22 | 073 | Maximum wave height |  |
|  | 0 | 22 | 074 | Average wave period |  |
|  | 0 | 22 | 071 | Spectral peak wave period |  |
|  | 0 | 22 | 076 | Direction from which dominant waves are coming |  |
|  | 0 | 22 | 077 | Directional spread of dominant wave |  |

This sequence is required for the representation of basic wave measurements from moored and drifting buoys.

3 02 Y18

Sequence for representation of detailed spectral wave measurements

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y18 |  |  |  | Sequence for representation of detailed spectral wave measurements |  |
|  | 0 | 22 | 078 | Duration of wave record |  |
|  | 0 | 22 | 082 | Maximum non-directional spectral wave density |  |
|  | 1 | 06 | 000 | Delayed replication of 6 descriptors |  |
|  | 0 | 31 | 001 | Delayed descriptor replication factor | Number of frequency bins |
|  | 0 | 22 | 080 | Waveband central frequency |  |
|  | 0 | 22 | 069 | Spectral wave density |  |
|  | 0 | 22 | 086 | Mean direction from which waves are coming |  |
|  | 0 | 22 | 087 | Principle direction from which waves are coming |  |
|  | 0 | 22 | 088 | First normalized polar coordinate from Fourier coefficients |  |
|  | 0 | 22 | 089 | Second normalized polar coordinate from Fourier coefficients |  |

This sequence is required for the representation of spectral wave measurements from moored buoys. It should be noted that the ability to report the spectra or statistical properties based on wave number is not included. As such this sequence is not suitable for the reporting of wave spectra from aircraft or satellites.

3 06 Y19

Depth and temperature profile (high accuracy / precision)

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 06 | Y19 |  |  |  | Depth and temperature profile (high accuracy / precision) |  |
|  | 0 | 02 | 032 | Indicator for digitization | Set to 0, fixed sensor depths |
|  | 1 | 02 | 000 | Delayed replication of 2 descriptors |  |
|  | 0 | 31 | 001 | Delayed descriptor replication factor | Number of depths |
|  | 0 | 07 | 062 | Depth below sea / water surface |  |
|  | 0 | 22 | 043 | Sea / water temperature |  |

This sequence is required for the representation of temperature profile data (to 2 decimal places) from moored buoys.

3 02 Y20

Wind measurement from drifting buoy

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | Y20 |  |  |  | Wind measurement from drifting buoy |  |
|  | 0 | 02 | 169 | Anemometer type | e.g. 2 = WOTAN, 3 = sonic anemometer |
|  | 0 | 07 | 033 | Height of sensor above water surface | Height of anemometer above water surface or effective height for WOTAN. |
|  | 0 | 08 | 021 | Time significance | Set to 2, time averaged |
|  | 0 | 04 | 025 | Time period or displacement | Averaging period in minutes |
|  | 0 | 11 | 001 | Wind direction | At measurement height |
|  | 0 | 11 | 002 | Wind speed | At measurement height |

This sequence is required for the representation of wind measurements from drifting buoys.

3 15 Y23

Dissolved oxygen profile data

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 15 | Y23 |  |  |  | Dissolved oxygen profile data |  |
|  | 1 | 09 | 000 | Delayed replication of 9 descriptors |  |
|  | 0 | 31 | 002 | Extended delayed descriptor replication factor |  |
|  | 0 | 07 | 062 | Depth below sea / water surface |  |
|  | 0 | 08 | 080 | Qualifier for quality class (set to 13, indicates depth at a level) |  |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 07 | 065 | Water pressure |  |
|  | 0 | 08 | 080 | Qualifier for quality class (set to 10, indicates pressure at a level) |  |
|  | 0 | 33 | 050 | GTSPP quality class |  |
|  | 0 | 22 | Y22 | Dissolved oxygen |  |
|  | 0 | 08 | 080 | Qualifier for quality class (set to 16, dissolved oxygen at a level) |  |
|  | 0 | 33 | 050 | GTSPP quality class |  |

This sequence is required for the representation of wind measurements from drifting buoys.

C.4 Proposed modifications to sequences

3 01 036

Ship location and identification sequence

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 01 | 036 | 3 | 01 | 003 | Ship’s callsign and motion |  |
|  |  |  | 0 | 02 | 001 | Type of station |  |
|  |  |  | 0 | 02 | YY9 | Surface station type |  |
|  |  |  | 3 | 01 | 011 | Year, month, day |  |
|  |  |  | 3 | 01 | 012 | Hour, minute |  |
|  |  |  | 3 | 01 | 023 | Latitude / longitude (coarse accuracy) |  |

Modified or inserted sequences are shown in red. The “surface station type” has been inserted as requested at the 7th JCOMM Ship Observations Team meeting. Sequence 3 01 003 has been modified to take the ENCODE proposal into account.

3 01 003

Ship’s callsign and motion

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 01 | 003 | 0 | 01 | 011 | Ship or mobile land station identifier |  |
|  |  |  | 0 | 01 | YY8 | Encrypted Ship or mobile land station identifier Ship's call sign |  |
|  |  |  | F | XX | YY6 | Encryption method used |  |
|  |  |  | F | XX | YY7 | Encryption key version |  |
|  |  |  | 0 | 01 | 012 | Direction of motion of moving observing platform |  |
|  |  |  | 0 | 01 | 013 | Speed of motion of moving observing platform |  |

The inserted descriptors are shown in red. These additions are described in the separate ENCODE proposal but have been included for completeness in this document.

3 02 052

Ship temperature and humidity data

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
| 3 | 02 | 052 | 0 | 07 | 032 | Height of sensor above marine deck platform (for temperature and humidity measurement) |  |
|  | 0 | 07 | 033 | Height of sensor above water surface (for temperature and humidity measurement) |  |
|  | 0 | 12 | 101 | Temperature / air temperature |  |
|  | 0 | 02 | 039 | Method of wet-bulb temperature measurement |  |
|  | 0 | 02 | YY2 | Ventilation method for humidity sensor |  |
|  | 0 | 02 | YY3 | Generic type of marine humidity sensor |  |
|  | 0 | 12 | 102 | Wet-bulb temperature |  |
|  | 0 | 12 | 103 | Dew-point temperature |  |
|  | 0 | 13 | 003 | Relative humidity |  |

The biases and error characteristics for humidity observations are known to vary significantly with the type of instrument used and the ventilation of the instrument. In order to take the different error characteristics and biases into account when assimilating the observations the UK Met Office has requested, via the JCOMM Ship Observations Team, that this information be included in the marine data template (B/C 10). The SOT-7 meeting noted and concurred with this proposal and this sequence has been updated to include that proposal. The associated code tables proposed below are based on the information typically collected and available from the WMO Publication No. 47.

C.5 Proposed new code / flag tables

0 02 YY2

Ventilation method for humidity sensor

| Code figure | Meaning |
| --- | --- |
| 0 | Aspirated |
| 1 | Screen (not ventilated, i.e. natural ventilation) |
| 2 | Screen (ventilated, i.e. assisted ventilation) |
| 3 | Ship’s screen (property of ship) |
| 4 | (Ship’s sling (property of ship) |
| 5 | Unscreened |
| 6 | Whirling or sling psychrometer |
| 7 – 14 | Reserved |
| 15 | Missing |

The values listed in this table have been taken from WMO Publication No. 47, the "International List of Selected, Supplementary and Auxiliary Ships". This publication lists the metadata and instrument methods for the majority of the Voluntary Observing Ship fleet.

0 02 YY3

Generic type of marine humidity sensor

| Code figure | Meaning |
| --- | --- |
| 0 | Capacitance |
| 1 | Chilled mirror |
| 2 | Electric |
| 3 | Hair hygrometer |
| 4 | Hygristor |
| 5 | Psychrometer |
| 6 | Torsion |
| 7 – 14 | Reserved |
| 15 | Missing |

The values listed in this table have been taken from WMO Publication Number 47. Either a new code table, as proposed, is needed to represent this information for the marine data or element 0 02 097 (Type of humidity sensor) needs to be expanded to accommodate the new values.

0 02 YY4

Method of sea / water current measurement

| Code Figure | Meaning |
| --- | --- |
| 0 | Reserved |
| 1* | ADCP (Acoustic Doppler Current Profiler) |
| 2 | GEK (Geomagnetic ElectroKinetograph) |
| 3 | Ship's set and drift determined by fixes 3-6 hours apart |
| 4 | Ship's set and drift determined by fixes more than 6 hours but less than 12 hours apart |
| 5 | Drift of buoy |
| 6 | ADCP (Acoustic Doppler Current Profiler) |
| 7 | ADCP (Acoustic Doppler Current Profiler) bottom tracking mode |
| 8 | Electromagnetic sensor |
| 9 | Rotor and vane |
| 10 | Lowered ADCP |
| 11 – 15 | Reserved |

This table is an expanded version of 0 02 030. A new table (and descriptor) is proposed due to the increased field width required. The new entries to this table are indicated in red.

0 02 YY5

Method of depth calculation

| Code figure | Meaning |
| --- | --- |
| 0 | Depth calculated using fall rate equation |
| 1 | Depth calculated from water pressure / equation of state |
| 2 | Reserved |
| 3 | Missing |

This table and associated descriptor are required to differentiate between the different methods of depth calculation for oceanographic data.

0 02 YY9

Surface station type

| Code figure | Meaning |
| --- | --- |
| 0 | Land station (synoptic network) |
| 1 | Shallow water station (fixed to sea / lake floor) |
| 2 | Ship |
| 3 | Rig / Platform |
| 4 | Moored buoy |
| 5 | Drifting buoy (or drifter) |
| 6 | Ice buoy |
| 7 | Land station (local network) |
| 8 | Land vehicle |
| 9 | Autonomous marine vehicle |
| 10 – 14 | Reserved |
| 15 | Missing |

0 02 Y21

Instrument type / sensor for dissolved oxygen measurement

| Code figure | Meaning |
| --- | --- |
| 0 | Anderraa oxygen Optode |
| 1 | Winkler bottle |
| 2 – 14 | Reserved |
| 15 | Missing |

C.6 Proposed modifications to code / flag tables

0 02 149

Type of data buoy

| Code Figure | Meaning |
| --- | --- |
| 4 | Ice float drifter |
| 38 | Ice beacon |
| 39 | Ice mass balance buoy |

The additions have been highlighted in red. The two new entries are needed to represent those types of data buoys. The renaming of ice float to ice drifter has been proposed to distinguish the entry from entry 30 (Ice buoy / float).

0 33 027

Location quality class

| Code Figure | Meaning |
| --- | --- |
| 4 | <= 100m |

The new addition has been highlighted in red. This is required to represent the increased accuracy available from GPS sensors.

0 08 029

Surface type

| Code Figure | Meaning |
| --- | --- |
| 18 | Sea ice |

The new entry has been highlighted in red. This is needed to distinguish between when the buoy is on ice or in the water.

0 22 067

Instrument type for water temperature profile measurement

| Code Figure | Meaning |
| --- | --- |
| 902 | Brooke Ocean Moving Vessel Profiler (MVP) |
| 903 | Seabird CTD |
| 904 | AML Oceanographic CTD |
| 905 | Falmouth Scientific CTD |
| 906 | Ocean Sensors CTD |
| 907 | Valeport CTD |
| 908 | Ocean Science MVP |
| 909 | Idronaut CTD |
| 910 | Seabird SBE38 |

These are additional entries for common code table C-3 (0 22 067) to provide more information about the types of CTD instruments typically used.

0 08 080

Qualifier for quality class

| Code Figure | Meaning |
| --- | --- |
| 14 | sea/water current speed at a level |
| 15 | sea/water current direction at a level |
| 16 | dissolved oxygen at a level |

Additional entries for quality class qualifier to include current speed and direction measurement at a level.

PART D - ADDITIONS TO REGULATIONS FORM B/C 10

The following additions to the “Regulations for reporting SHIP data in TDCF” are proposed:

B/C 10.4.4.1:

2) When cloud cover is observed in Oktas the cloud cover shall be converted to percent, with fractional numbers rounded up (e.g. 1 Okta = 12.5%, rounded to 13 %).

B/C 10.10	The element descriptor 2 05 YYY shall be included as the last element in all synoptic reports for sea stations, i.e. the data descriptors in Section 3 of the BUFR message for VOS shall be given by 3 08 009 2 05 YYY. The element 2 05 YYY shall include the synoptic report in its original form as reported and the YYY in the descriptor replaced by the number of characters in this element.

____________

Appendices: 2

APPENDIX A

Excerpt from the final report of the 7th session of the JCOMM Ship Observations Team (section 9.2.1).

9.2.1 BUFR Template for VOS data

BUFR Templates

9.2.1.1	The Team recalled that WMO Commission for Basic Systems (CBS) migration to table driven codes for marine data shall be completed between November 2012 and November 2014 per CBS-Ext. (2010) recommendation (Appendix F). The Team recognized that progress with regard to the development and updating of the required BUFR templates for marine meteorological and oceanographic data has been limited since the sixth SOT Session (Hobart, Australia, April 2011).

9.2.1.2	The Team noted and concurred with a proposal from the UK MetOffice to add “Surface station type”, and “Generic type of humidity instrument” is marine data BUFR templates (Appendix I). The Team urged the Task Team on Table Driven Codes (TT-TDC) to speed the submission of SOT related BUFR template proposals to the CBS taking SOT requirements into account (action: TT-TDC; ASAP). However, the Team noted with concern that the TT-TDC had currently no Chair, and was not active. It requested the Secretariat to investigate for the nomination of a new chair in consultation with the Chair of DMCG (action; Secretariat; ASAP).

9.2.1.3	The Team noted that plans are underway for sharing tools for BUFR encoding/decoding software within the oceanographic community, and example of BUFR reports have been produced for training purposes (there have been recorded in the IODE OceanTeacher). It was also noted that JCOMM-4 requested the DMPA to keep the “Cookbook for submitting ocean data in real-time and delayed mode” under review, and continue to keep the BUFR templates for ocean data under review so that they continue to take end-user requirements into account. Highlighting the importance of BUFR, JCOMM-4 further requested the DMPA to finalize the BUFR Master Table 10 (Oceanographic Data).

9.2.1.4	The Team recalled that JCOMM has engaged a process for the rationalization of BUFR sequences for marine data in order to provide some standardization and consistency for the reporting of specific ocean variables and their metadata between the different types of ocean observation platforms reporting in BUFR format (e.g. same sequence for data and metadata for SST observations from VOS, moorings, drifters, tide gauges, etc.). Details are provided in Appendix E.

9.2.1.5	See also agenda item 6.6 (and corresponding SOT-7 preparatory document) relating to the provision of encrypted ship’s call sign (ship masking) within the BUFR template for VOS data.

Preservability of marine data

9.2.1.6	Regarding the issue of preservability of the real-time data, the Team recalled that the ETMC had established a small ad hoc group at its third meeting (Melbourne Australia, February 2010) to address each of the following levels:

- Observing practices and the recording of the observations on-board the ship;

- Transmission of the observations in real-time from ship to shore. While it was not proposed to standardize the format(s) used for the transmission of VOS data from ship to shore, the Team felt that it would be useful to provide guidance regarding the elements that should be transmitted, on a variable-by-variable basis; and

- Transmission of the observations in real-time onto the GTS in BUFR format.

9.2.1.7	The Team recalled that the ad hoc group had produced a report (Appendix C) that was then submitted to the sixth Session of the Ship Observations Team (SOT-6, Hobart, 11-15 April 2011). The Team recalled the recommendations from SOT-6 in this regard (Appendix D).

9.2.1.8	The Fourth Session of the ETMC (Ostend, Belgium, November 2012) recognized that there has not been sufficient validation of the existing BUFR templates for marine meteorological and oceanographic data, and agreed that the ICOADS should have been involved in the validation. ETMC-4 noting outstanding issues, agreed to re-activate the ad hoc group on preservability, and requested it to address the SOT-6 decisions, and to make further proposals to this SOT Session, especially regarding practices to be included in the section of the Guide to Marine Meteorological Services (WMO No. 471) describing the VOS Scheme and in the Manual on Codes (WMO No. 306). The ETMC-4 requested the ad hoc group to address the SOT-6 decisions, and to make further proposals to this SOT Session. The recommendations form the ad hoc group are provided in Appendix G. The Team concurred with the following recommendations from the ad hoc group:

- 2a) Recommendation: Endorse and encourage the creation of a permanent and open repository for the storage and provision of past observing instructions and regulations within the CMOC framework.

- 2b) Recommendation: encourage the use of the above mentioned repositories for storing old e-logbook documentation and source code where software licensing allows.

- 2c) Recommendation: Encourage the use of e-logbook and AWS manufacturers that support the archival of old versions and documentation.

- 3a) Recommendation: support the creation of a new E-SURFMAR data format for non AWS VOS based on data format #100 with the conventional VOS section expanded to include either both the dew point temperature (replacing relative humidity) and wet bulb temperature to 0.1°C or the relative humidity together with a flag indicating the humidity variable reported.

- 4a) Recommendation: Update B/C 10 to reflect that cloud is typically observed in Oktas and give guidance on the coding of this in % by the addition of the following note to B/C 10.4.4.1:

2)	When cloud cover is observed in Oktas the cloud cover shall be converted to percent, with fractional numbers rounded up (e.g. 1 Okta = 12.5%, rounded to 13 %).

- 4b) Recommendation: Support the further development of the common marine sequences, with an aim to submitting a new BUFR template proposal, including table revisions, to the Autumn IPET-DRC meeting.

- 4c) Recommendation: For an initial period(a minimum of 2 years) an additional descriptor is included in the BUFR / CREX template for VOS reports giving the report in its original form before encoding into BUFR. This would require the addition of the following regulation to B/C 10 (and any update):

B/C 10.10	The element descriptor 2 05 YYY shall be included as the last element in all synoptic reports for sea stations, i.e. the data descriptors in Section 3 of the BUFR message for VOS shall be given by 3 08 009 2 05 YYY. The element 2 05 YYY shall include the synoptic report in its original form as reported and the YYY in the descriptor replaced by the number of characters in this element.

- 4d) Recommendation: For an initial transition period of at least two years, the VOS reports shall also be distributed in parallel over the GTS in FM13 or the CREX format using the agreed BUFR / CREX template.

9.2.1.9 Regarding Recommendation 3a, the Team requested E-SURFMAR to finalize the proposed new data format for non AWS VOS, and liaise with the ETMC ad hoc group in this regard. The goal is to have the new format eventually approved by the VOSP Chair (action; P. Blouch; end 2013).

9.2.1.10 The Team noted that ETMC-4 has requested David Berry (UK) to coordinate with Joaquin Trinanes in the view to submit a CTD BUFR template to the DMPA Task Team on Table Driven Codes (TT-TDC) for their review, and further submission to the CBS.

9.2.1.11 The Team requested the Sub-Group on AWS of the TT-IS to look at the issue of preserving AWS data, and to make recommendations in this regard at the next SOT Session (action; TT-IS/SG-AWS; SOT-8).

APPENDIX B

status of BUFR templates for marine data AS REPORTED TO THE 7th SHIP OBSERVATIONS TEAM (SOT-7)

|  | Current template(s) | Status | Plans/comments |
| --- | --- | --- | --- |
| Drifting buoy data | Template for buoy data including directional and non-directional wave data | Validation | Template is currently the same for drifting, moored, and wave buoys. The plan is to produce a specific simplified template for drifting buoys |
| Moored buoy data | Template for buoy data including directional and non-directional wave data | Validation | Template is currently the same for drifting, moored, and wave buoys. The plan is to produce a specific simplified template for moored buoys |
| Wave buoy data | Template for buoy data including directional and non-directional wave data | Validation | Template is currently the same for drifting, moored, and wave buoys. The plan is to produce a specific simplified template for wave buoys |
|  | Templates for the wave observations from different platforms suitable for WAVEOB data | Validation | Template should undergo validation |
| VOS data | B/C10 - Regulations for reporting SHIP data in TDCF | Operational (TM308009) | No specific plan for this template |
|  | Synoptic reports from sea stations suitable for SHIP observation data from VOS stations (see Appendix B) | Validation | Template should be revised to allow for the encryption of the ship’s call sign. |
| ASAP data | B/C25 - Regulations for reporting TEMP, TEMP SHIP, TEMP MOBIL data in TDCF | Operational (TM309052) | No specific plan for this template |
|  | UKMO template for representation of radiosonde data with geopotential height as the vertical coordinate | Operational (revisited in July 2010) | The former EUCOS template for radiosonde data with geopotential height as the vertical coordinate is deprecated, and its specific requirements included in the UKMO template for the representation of radiosonde data with geopotential height as the vertical coordinate (the vertical resolution is limited by the length of BUFR message). See annex to paragraph 3.3.6 of the final report of the 3rd meeting of the IPET-DRC (Melbourne, Australia, 2011) |
| XBT data | New BUFR template for XBT Temperature Profile data | Operational (TM315004) as from 7 Nov. 2012 |  |
| Argo data | Sub-surface profiling floats | Operational (TM315003) | No specific plan for this template |
| TRACKOB data | TRACKOB data – ThermoSalinoGraph (TSG) data and metadata | Operational (TM308010) | No specific plan for this template |
| CTD | None | Efforts initiated | There is not BUFR template for the reporting of CTD measurements made by ships. Bob Keeley (Canada) and Joaquin Trinanes (USA) have discussed a BUFR template for CTD data, which may have to be submitted to CBS. ETMC-4 invited David Berry (UK) to coordinate with Joaquin Trinanes in the view to submit the template to the TT-TDC for their review, and further submission to the CBS |
| Sea-level data | BUFR/CREX templates for tsunameter data and dart buoy system messages | Operational (TM306027) | No specific plan for this template |
|  | BUFR/CREX templates for reporting time series of tide data | Validation | Template should undergo validation |

# Footnotes

http://icoads.noaa.gov/etmc/ETMC4-Doc-5.2-REV1-BUFR.pdf

http://jcomm.info/index.php?option=com_oe&task=viewEventDocs&eventID=1193

http://icoads.noaa.gov/

http://www.jcommops.org/dbcp/data/metadata.html

http://www.wmo.int/pages/prog/www/ois/pub47/pub47-home.htm

Completion means that at this date the BUFR (CREX) exchange becomes the standard WMO practice. Parallel distribution of TAC and TDCF may continue and will be discontinued within a zone in accordance with step-by-step arrangements made between the NMHS concerned. Details in annex XI of the abridged final report with resolutions and recommendations of CBS-Ext (2010), Windhoek, Namibia, 17–24 November 2010 – http://www.wmo.int/pages/prog/www/CBS/Reports/2010_Ext10_Windhoek_1070/1070_en.pdf

:	FM-94 BUFR : Binary Universal Form for the Representation of Meteorological Data (used for distribution of time critical data onto the Global Telecommunication System – GTS.

http://library.oceanteacher.org/OTMediawiki/index.php/BUFR_and_GRIB_Formats

http://www.jcomm.info/index.php?option=com_content&task=view&id=37&Itemid=49

The group is comprised of Gudrun Rosenhagen (Germany), Shawn Smith (USA), David Berry (UK), Nicola Scott (UK), and Scott Woodruff (USA)

http://www.wmo.int/pages/prog/www/ISS/Meetings/IPET-DRC_Melbourne2011/Report/Report_IPETDRC-III_Melbourne2011.doc

Conductivity, Temperature, and Depth