PROUDMAN OCEANOGRAPHIC LABORATORY

CRUISE REPORT NO.  46

RRS JAMES CLARK ROSS

OCTOBER 27, 2003 – NOVEMBER 22, 2003

ACCLAIM: Sea Level Measurements in the Drake Passage and Scotia Sea

S. Mack

2004

DOCUMENT DATA SHEET

| AUTHOR S. Mack | PUBLICATION DATE 2004 |
| --- | --- |

TITLE RRS James Clark Ross, October 27, 2003 – November 22, 2003 ACCLAIM: Sea Level Measurements in the Drake Passage and Scotia Sea

REFERENCE Proudman Oceanographic Laboratory, Cruise Report, No 46, 10 pp.

ABSTRACT ACCLAIM Bottom Pressure Recorders have been used for making measurements of the Antarctic Circumpolar Current (ACC) since 1988, initially in the Scotia Sea and then later across the Drake Passage between the Falkland Islands and the Antarctic peninsula. Some of the Bottom Pressure Recorders (BPRs) are combined with Inverted Echo Sounders (IES) and deployed along the track of TOPEX/POSEIDON satellites that collect altimeter data from the area. The Sea Level Recorders at Stanley, and Signy were serviced.

| ISSUING ORGANISATION Proudman Oceanographic Laboratory Bidston Observatory Bidston Prenton CH43 7RA UK Director: Dr A.E Hill | TELEPHONE: (0151) 653 8633 FAX: (0151) 653 6269 TELEX: 628591 OCEAN BG |
| --- | --- |

| KEYWORDS Bottom Pressure Recorder Drake Passage Inverted Echo Sounder MYRTLE Sea Level Antarctic Circumpolar Current CROCUS Scotia Sea | CONTRACT PROJECT 3310 MXX 03205 PRICE £10.00 |
| --- | --- |

Copies of this report are available from:

The Library, Proudman Oceanographic Laboratory.

CONTENTS

CRUISE PERSONNEL					2

ACKNOWLEDGEMENTS					2

OVERVIEW					2

POL CRUISE OBJECTIVES					3

SHIP PREPARATION					3

## SERVICING STANLEY SEA LEVEL RECORDER 			3

DEPLOYMENT OF DRAKE PASSAGE NORTH CROCUS BPR		4

RECOVERY OF MYRTLE (POL 11)					4

SERVICING SIGNY SEA LEVEL RECORDER				4

APPENDIX 1 - BPR TECHNICAL INFORMATION			6

STANLEY SEA LEVEL RECORDER INFORMATION		6

## SIGNY SEA LEVEL RECORDER INFORMATION		6

DRAKE PASSAGE NORTH BPR (POL 8) DEPLOYMENT	7

MYRTLE (POL11) RECOVERY INFORMATION			8

MAP OF DEPLOYMENT POSITIONS					10

GLOSSARY									11

# CRUISE PERSONNEL

POL Personnel

Higher Scientific Officer		Geoff Hargreaves

Higher Scientific Officer		Steve Mack

Ship Personnel

Captain				Christopher Elliot

Chief Officer				Robert Patterson

Second Officer				Andy Liddell

Third Officer				Mike Golding

Chief Engineer				Dave Cutting

Second Engineer			Gerry Armour

Bosun					George Stewart

# ACKNOWLEDGEMENTS

The author would like to thank the Captain, Officers and ship's company of RRS James Clark Ross for their help in the deployment and installation of sea level equipment and the British Antarctic Survey for the opportunity to perform this work. The author would also like to thank the personnel of Signy base, for their help and support in servicing and maintaining our Sea Level Recorders.

# OVERVIEW

ACCLAIM - Antarctic Circumpolar Current Levels from Altimeter and Island Measurements is providing real time data from it's network of sea level stations in the Southern Ocean as a contribution to the World Ocean Circulation Experiment (WOCE). The associated research work at POL is an integral part of the many other UK contributions to Core 2, the Southern Ocean component of WOCE, and interacts with international work from the United States, South Africa, Australia, France and Germany. The principal objective is to study variations in the flow of the Antarctic Circumpolar Current (ACC) on large time and space scales, however the ACCLAIM network is also a component of GLOSS (Global Sea Level Observing System). These BPR’s have supplied sea level data that has provided knowledge of tidal behaviour in this remote area.

ACCLAIM Bottom Pressure Recorders (BPR’s) have been deployed since 1988, initially in the Scotia Sea and then later in the Drake Passage. Bottom Pressure Recorders are currently deployed in both locations to further aid the investigation of the ACC.

# POL CRUISE OBJECTIVES

# 1) To service and repair the Sea Level recorder at Stanley, Falkland Islands.

# 2) To deploy a Crocus BPR in the Drake Passage (Drake North).

# 3) To recover MYRTLE from the Scotia Sea.

# 4) To service the Sea level recorder at Signy.

## SHIP PREPARATION

POL personnel Geoff Hargreaves and Steve Mack arrived in the Falkland Islands 25/10/03 and started servicing the Stanley Sea Level Recorder. Joined ship on 28/10/03 and located and prepared equipment for deployment of Crocus and MYRTLE recovery.

## SERVICING STANLEY SEA LEVEL RECORDER ( 27-30/10/03 )

The Stanley Sea Level Recorder (SLR) consists of two logging systems, one measuring tidal information and the other measuring wave information. The tide logger samples data every 15 minutes. The wave logger (CF1) samples data every one second and is connected to the telephone network via a modem. This system (CF1) also emails data back to POL automatically every hour using a web-modem.

Problems were occurring in dialling in to the CF1 system. A connection could not be established via the modem on numerous attempts from the UK. This was also the case when testing from a phone from the Falkland Islands. Several attempts were made to resolve the problem. All cards and modems were replaced with a equipment that had worked under test in the UK. A more substantial earth was used for the CF1 system and Cable and Wireless were contacted to perform a test on the telephone line to the gauge. All these attempts were unsuccessful at this pre-cruise time.

The tide logger was operating perfectly well. The data stored locally was downloaded and timing errors were noted. The logger was then re-started.

Stanley Sea Level Recorder Servicing Summary

Servicing the tide logger went smoothly and the data was successfully recovered. The wave logger proved more troublesome and could not be repaired during this visit.

## DEPLOYMENT OF DRAKE PASSAGE NORTH CROCUS BPR 31/10/03

EVENTS

1450 GMT		-	Vessel on station

1459 GMT		-	Released into the water

Total time on station: 9 minutes

### Drake Passage North CROCUS BPR Deployment Summary

This Crocus was deployed to replace the BPR that couldn’t be recovered in 2002.

This CROCUS BPR was deployed successfully. The weather was quite rough (force 8/9). The unit was not monitored down to the seabed due to the weather conditions.

## RECOVERY OF MYRTLE (POL 11) 03/11/03

EVENTS

0916 GMT			Vessel on station.

0920, 0923 GMT		Release command transmitted.

1021 GMT			On the surface.

Total time on station: 1 hour 5 mins

### MYRTLE Recovery Summary

Recovery went vary smoothly. Acoustic conditions were very quiet for the recovery. All acoustics were tested and all responded well. Both acoustics were fired. Ascent to surface was slower than expected and on surface frame was listing. This was found to be due to a leaked sphere.

## SERVICING SIGNY SEA LEVEL RECORDER 27/10/1999

The Sea Level Recorder is situated in the loft of the generator shed and is housed in a metal enclosure, which in turn is fitted inside a wooden crate insulated with polystyrene, to try and give some protection from the severe cold temperatures that are experienced during an Antarctic winter. The sea sensors are situated in the middle of the bay, laying on the sea floor and are connected to the logger by armoured cable. This system has two modes of operation: winter and summer. During the summer, when the base is occupied, the system runs off trickle charged batteries from the electricity supply and during the winter it runs off lithium batteries. This was the first call of the summer season to Signy so the system was still set to winter mode of operation.

On inspection of the system no scan was observed. Batteries were tested and were flat. New batteries were fitted and it was attempted to download the data from the SRAM card. It appeared blank and so no data was downloaded. This card was removed and replaced with a new one. A binary dump of the old card was taken for further investigation. The Toshiba laptop was installed but not powered up due to lack of mains power. The system was re-started and left running on battery power.

### Servicing Signy Sea Level Recorder Summary

The Sea Level recorder was left in a working state and the base staff were left with instructions to switch to mains power when the generators were up and running. The Lithium batteries were flat and no data was found on the SRAM card. The reason for this is not yet known.

# APPENDIX 1 - BPR TECHNICAL INFORMATION

## STANLEY SEA LEVEL RECORDER INFORMATION

Sensors fitted.

Full Tide	DQ 47594

Half Tide	DQ 47598

Barometer	DQ 39239

Scan Expected 	124500 GMT

Actual scan timed 	124427 GMT  27/10/03

Data downloaded to stan03002.

SRAM card replaced and logger restarted.

First SRAM card was faulty so no data recorded until checked on 29/10/03

Timebase started	191500 GMT  29/10/03

First Scan 		193000 GMT

## SIGNY SEA LEVEL RECORDER INFORMATION

The sea level recorder at Signy consists of a sensor housing, placed on the seabed in the middle of the bay, connected to the shore by armoured cable. The logging electronics are situated in the loft of the generator shed, housed inside a metal box that is installed inside a polystyrene insulated wooden crate. The insulated wooden crate is used to protect the system during the Antarctic winter when the base is closed, and no heating is available. The SLR has two operational modes: summer and winter. During summer operating mode, the system runs off the base mains supply with a trickle charged backup battery. For winter use, three high capacity lithium batteries are used and a switch is fitted to change over from summer to winter operation.

Timing Information

Logger started 153000 GMT	04/11/03

154500 GMT

Batteries

Batteries flat- measured at 4.95V

No data recovered from over winter. SRAM card replaced and old card removed for investigation.

Sea Level Recorder was left running on new batteries as generator was not running at the time. Instructions left to switch to mains.

## DRAKE PASSAGE NORTH BPR (POL 8) DEPLOYMENT INFORMATION

Location details			-	Latitude	54° 56.59’ S									Longitude	58° 21.41’ W									Depth		1148 m

On station				-	1450 GMT on 31/10/03

Released into the water		-	1459 GMT

Acoustic Information

Benthos TR7000 Acoustic Release SN 61199

Tx = 12.00 kHz	Rx = 11.00 kHz	ID = 05

A= Enable, B = Disable, C = Release, D = Ping

Release type: Burnwire

Enable gives a 4 ping acknowledge, then 1 ping returns 1 ping.

On Release there is NO acknowledge. After timeout (~60secs) one ping sent gives 4 ping return.

Subsequent release commands will toggle release from on to off but still give 4 ping return.

.

Logger

Logger P3 fitted with sensor DQ68485

Timebase started at 231500 GMT on 29/10/03

First scan at 233000 GMT

Radio Beacon

Benthos radio beacon			-	154.585MHz

Channel A

New Battery Information

Acoustic battery			-	Upper : Red	14.48V

Orange 14.49V

Lower: Red	14.47V

Orange	14.49V

Burnwire battery			-	28.10V

Logger battery				-	Red	14.74V

Orange	14.75V

MYRTLE (POL11) RECOVERY INFORMATION

Location details			-	Latitude	60( 02.98' S

Longitude	047( 10.20' W

Depth	2354m

On station				-	0916 GMT	03/11/03

Release command sent			-	0920, 0923 GMT

On the surface				-	1021 GMT

Acoustic Information

Main frame release 51314		-	Rx 14.5kHz, Tx 12.0kHz, Release A

Main frame release 51329		-	Rx 10.0kHz, Tx 12.0kHz, Release D

Main pod release			-	Rx 11.0kHz, Tx 12.0kHz,

Satpod A, Pod2 B, Pod3 C, Pod4 D

Secondary pod release			-	Rx 11.5kHz, Tx 12.0kHz,

Pod2 C, Pod3 D, Pod4 E

Podule transponders			-	Satpod		-	none fitted

Pod2		-	Rx 12.5kHz, Tx 12.0kHz

Pod3		-	Rx 10.5kHz, Tx 12.0kHz

Pod4		-	Rx 13.0kHz, Tx 12.0kHz

Logger

Timebase: Last scan at 194934 GMT on 05/11/03

Expected on 210000 GMT

Pod2

Batteries disconnected and sphere sealed

Pod3

Pod 3 leaked so batteries removed. Electronics left inside.

Pod4

Batteries disconnected and sphere sealed.

Recovery Equipment

Benthos radio beacon on Pod2		-	154.585 MHz, Channel A

Benthos radio beacon on Pod3		-	154.585 MHz, Channel A

Benthos radio beacon on Pod4		-	154.585 MHz, Channel A

Batteries

Main frame acoustic release (51314)	-	Red	-

Orange	-

Main frame acoustic release (51329)	-	Red	-

Orange	-

Main pod acoustic release (48513)	-	External Batts

Secondary pod acoustic release	-	Red	12.14V

Orange	12.14V

Pod2 acoustic battery			-	Red	14.34V											Orange	14.34V

Pod2 logger battery			-	Red	12.92V

Orange	12.92V

Pod3 acoustic battery			-	Leaked

Pod3 logger battery			-	Leaked

Pod4 acoustic battery			-	Red	14.38V

Orange	14.39V

Pod4 logger battery			-	Red	12.87V

Orange	12.87V

Main Logger				-	Red	13.95V

-	Orange	13.56V

# MAP OF DEPLOYMENT POSITIONS

# GLOSSARY

ACCLAIM      -	Antarctic Circumpolar Current levels from Altimeter and Island Measurements

BPR		-	Bottom Pressure Recorder

CROCUS	-	Capsule for the Recovery of Ocean Circulation Under the Sea

DCP		-	Data Collection Platform

EPROM	-	Erasable Programmable Memory

FIPASS	-	Falkland Islands Passenger and Sea Service

GMT		-	Greenwich Mean Time

IES		-	Inverted Echo Sounder

MYRTLE	-	Multi-Year Return Tidal Level Equipment

POL		-	Proudman Oceanographic Laboratory

SLR		-	Sea Level Recorder

SRAM		-	Static Random Access Memory

TDS		-	Triangle Digital Services

WOCE		-	World Ocean Circulation Experiment